WVSC Sewage System Winterization

- Connect the boat pump-out hose use lake water to flush all sewage in the basin and line for 20-30 minutes.

- Connect the pump-out hose and put the inlet in the lake to draw in lake water

- Select Pump-out pump switch to ON

- Set Clubhouse sewage pump switch to HAND (On)

When complete:

d.	Select pump-out pump switch to OFF

e.	Select sewage pump switch to AUTO

f.	Stow pump-out hose

- Open the ball valves on both sides of the check valve on the north side of the holding tank inside the dry storage fence.

- Position the pump truck on the west ramp close to the pump-out port near the steps of the bridge to the walkway.  There are two ball valves located to each side of this pump out port. Close the ball valve to the north of the pump-out port and pump down sewer line leading to the holding tank.

- Now open the north ball valve and close the one to the south. This will draw any water in the holding basin through the pump and evacuate the sewer line on the water and across the bridge.

- Listen to the pipe on either side of the valves;

- When it sounds as if only air is passing through the lines, close the valve on the truck’s pump out hose and allow the truck to build vacuum to about 15 -18ins.  Re-open the south valve and close the north.  Open the truck’s pump out hose valve and listen to the pipe for water surging through the line.

- Repeat this process with the north valve open and the south valve closed.  Listen to the pipe to insure that all fluid is drawn out.  If there is water in the line, you will hear gurgling.

Close both valves and let the vacuum truck build up about 15-18 inches of vacuum and open one valve.  If the line is empty, the vacuum gauge will drop to about 5 inches immediately.  If the vacuum drops immediately, close the valve and repeat this process for the other valve.

- At this point the pump out process is completed and the truck is no longer needed.

- Close ball valves on the north side of the holding tank in Dry Storage area.

- Add antifreeze to the following:

Dump one gallon in each of the three risers between the docks and  storage tank.  This will protect the low spots in the line.

Dump five gallons into the boat pump-out connection on the east side of the walkway run the pump until you hear “gurgling from the connection.  This will ensure the line, pump and the sewage basin have sufficient antifreeze to prevent freezing over the winter.  Run the sewage pump to move some of the antifreeze into the line under the walkway.

- Turn off circuit breakers to the pump out system (breakers 01 & 03 “PUMP OUT PUMP”) and to the sewage pump (breakers 04 & 06 “SEWER PUMP”).

WARNING: PLACE A TIE WRAP THROUGH THE CIRCUIT BREAKER LOCKS SO THE CIRCUIT BREAKERS CANNOT BE INADVERTANTLY TURNED ON.